## Slide 1: A new tool for Determining subsurface LNAPL Volume and Extent
Phillip C. de Blanc, Ph.D., P.E.
pcdeblanc@gsi-net.com
GSI Environmental Inc.
2211 Norfolk St., Suite 1000
Houston, Texas 77098
www.gsi-net.com
25TH IPEC: International Petroleum Environmental Conference
October 30 – November 1, 2018 Denver, Colorado
Shahla K. Farhat, Ph.D.
skfarhat@gsi-net.com

## Slide 2: the LNAPL problem…
How much LNAPL is down there?
How much is potentially recoverable by conventional technologies?
If it’s recoverable, where should the recovery wells be located?

## Slide 3: LNAPL in formation and a monitoring well
Formation
LNAPL Saturation
50
75
100
25
0
Oil Water Air
Fraction of
Fluid in Pore Space
0 20 80
5 45 50
60 40 0
30 70 0
10 90 0
0 100 0
In Well
Oil/water Interface
Oil/air Interface
Oil Saturation Curve
bo (apparent
thickness)

## Slide 4: definition of specific volume
Do
Do: Volume of LNAPL in a formation per unit area.

## Slide 5: specific volume depends on the soil type
Loamy Sand
Silty Sand
Silty Clay
Key idea: For the same observed LNAPL thickness in a monitoring well, the volume of LNAPL in the formation depends on the soil type.

Residual LNAPL
Mobile LNAPL

## Slide 6: Do Calculation - current approach
Calculate specific volume (Do) at each monitoring well
  Screen out invalid measurements
  Use a tool (e.g., API LDRM) to estimate Do and Tn at each location
Interpolate point estimates of Do using software like GMS, Surfer, etc.
Sum the values within or external to the software to determine total LNAPL volume

## Slide 7: current approach

## Slide 8: current approach – ldrm interface
User specifies soil properties for each location/time.
User specifies LNAPL and water levels for each location/time/layer
This approach works well when data is limited both spatially and temporally.
User specifies layer interface for up to 3 layers

## Slide 9: motivation for a different approach

## Slide 10: the solution…
Perform same calculations as LDRM in a spreadsheet
Link spreadsheet calculations to data to avoid time-consuming re-entry of data into LDRM
  Water levels
  Apparent LNAPL thicknesses
  Soil types and position of wellscreens
Complete interpolation in spreadsheet to calculate total LNAPL volumes and distribution of Do and Tn

## Slide 11: on each row, the spreadsheet brings together:
Stratigraphy Database
LNAPL and Water Level Measurements
Database
Soil Properties
Database
LNAPL
Properties
Well Construction
Database
Clay
Sand
Silty clay
Clay
Sandy silt
Sand
Silty sand
Clay
Sand
Sandy silt

## Slide 12: bringing it all together
Stratigraphy Database
LNAPL and Water Level Measurements
Database
Soil Properties
Database
LNAPL
Properties
Well Construction
Database
Do = 3 ft; Dom = 2.4 ft; Tn = 31 ft2/d
Do, Dom, and Tn are calculated simultaneously on a single row for each measurement event.

## Slide 13: what the spreadsheet looks like

## Slide 14: what the spreadsheet looks like

## Slide 15: spreadsheet also includes single well evaluation

## Slide 16: the calculations (nerd alert!)
Specific Volume:
Mobile Volume:
LNAPL Transmissivity:

## Slide 17: how the calculations are done on a single line: vba code

## Slide 18: interpolation of do and Tn
Publicly available module for Excel
  XonGrid Interpolation Add-in
  http://xongrid.sourceforge.net/
  Author: Benjamin Deglo de Besses
  Copyright 2010, 2013, 2014
Methods:
  Natural neighbor
  Inverse-distance weighted
  Kriging
Calculated in spreadsheet using array formulas (no separate step is needed)

## Slide 19: an example (hypothetical)
How much LNAPL is down there?
How much is potentially recoverable by conventional technologies?
If it’s recoverable, where should the recovery wells be located?

## Slide 20: Data from an lnapl investigation and apparent volume
Apparent volume = 980,000 ft3 (7.3 million gal)
LNAPL
Apparent
Thickness
(bo, in feet)
Groundwater elevation contour (ft msl)

## Slide 21: how much is down there?
Total volume based on Do interpolation = 97,000 ft3 (730,000 gal)
LNAPL
Apparent
Thickness
(bo, in feet)
Apparent volume = 980,000 ft3 (7.3 million gal)
Specific volume (Do) contour (ft)
Use spreadsheet to calculate Do on a regular grid from data in databases.

## Slide 22: how much is recoverable?
Total mobile volume = 25,000 ft3 (190,000 gal)
Mobile volume (Dom) contour (ft)
LNAPL
Apparent
Thickness
(bo, in feet)
Use spreadsheet to calculate Dom on a regular grid from data in databases.

## Slide 23: where should recovery wells be located?
Point: Areas of high transmissivity do NOT necessarily correspond to locations of greatest apparent LNAPL thickness.

LNAPL transmissivity (Tn) contour (ft2/day)
LNAPL
Apparent
Thickness
(bo, in feet)
LNAPL Transmissivity calculation

## Slide 24: where should recovery wells be located?

## Slide 25: where should recovery wells be located?

## Slide 26: other uses of the spreadsheet tool
Compare many measurements at same location to determine maximum specific volume
Use tool to calibrate residual saturations in unsaturated and saturated zones
Rapidly screen out invalid measurements (LNAPL not fully within wellscreen)
Determine where LNAPL is accumulating or decreasing at an individual location

## Slide 27: CONCLUSION
Spreadsheet tool offers many advantages over the LDRM in terms of efficiency and capabilities for calculating Do, Dom, and Tn.
Automatic calculation of LNAPL volume and locations of maximum Tn are very helpful in LNAPL remediation projects.
You can spend a lot of time (not) perfecting PowerPoint animations!

## Slide 28
Funding needed for further development!
END
Phillip C. de Blanc, Ph.D., P.E.
pcdeblanc@gsi-net.com
2211 Norfolk St., Suite 1000
Houston, Texas 77098
713-522-6300

## Slide 29: comparison of new tool to conventional ldrm method
CATEGORY | LDRM | SPREADSHEET TOOL
Efficiency | One-by-one evaluation of each measurement event. | Simultaneous evaluation of an essentially unlimited number of events using information from spreadsheet databases.
Stratigraphy | Stratigraphy must be re-defined for every measurement event if LNAPL falls outside of initial range. Limited to 3 layers. | Stratigraphy is defined only once for each location and covers a much larger depth range. Currently 10 layers with unlimited capability for expansion.
LNAPL and water levels | Each bo and SWL measurement event must be manually entered by location and date. | Once database is created, all LNAPL thickness and SWL measurements are evaluated simultaneously.
Soil characteristics | Soil characteristics must be manually entered. | Spreadsheet database of soil types allows pre-definition of unlimited number of parameter sets.
Calculation results | Calculated Do, Dom and Tn values must be manually entered into other software for further evaluation. | Do, Dom, and Tn values for each measurement event are present in cells that the spreadsheet tool can use immediately for calculations or for export.
Total LNAPL volume calculations | Total LNAPL volume and mobile volume are not directly calculated. | Total LNAPL volume and mobile volume are calculated directly within spreadsheet using the interpolated values.
Interpolation | Calculated Do, Dom, and Tn values must be exported to other software for interpolation. | Interpolation is completed directly in spreadsheet based on user-specified grid and interpolation method.