## Slide 1
Concerns Over the Use of Geomembrane Liners as an Engineering Control for the Long-Term Storage of Oil and Gas Wastes
IPEC 2018. Denver, CO. Jeff Tyson, P.E.

## Slide 2: Outline
Introduction
Waste Characteristics
Potential Impact
Degradation of Geomembrane Liners
Conclusion

## Slide 3
E&P Wastes – Drilling Wastes
Rock cuttings and fluids that are produced during drilling
1.2 barrels of waste generated per foot drilled
  Average 50% solids / 50% liquids
392,000,000 bbls generated in 2014
  ~94.7 million tons
http://canstrat.com/learningcentre/33-what-you-should-know-about-drill-cuttings.html

## Slide 4
Contaminants in Drilling Waste
Metals
  Arsenic
  Barium
  Cadmium
  Chromium
  Lead
  Mercury
  Selenium
  Silver
  Zinc
Salts
  Chlorides
  Nitrates
Organics
  Hydrocarbons
  Benzene
pH
Other Contaminants

## Slide 5
Geomembranes
Common Types of Geomembranes
  HDPE = high density polyethylene
  LLDPE = linear low density polyethylene
  FPP = flexible polypropylene
  PVC = polyvinyl chloride (plasticized)
  CSPE = chlorsulfonated polyethylene
  EPDM = ethylene propylene diene terpolymer
Geomembranes are formulated and selected based on use

## Slide 6
Engineering and Institutional Controls
Engineering Control (ITRC)
  Physical modifications to a site or facility to reduce or eliminate the potential for exposure to residual contamination (for example, slurry walls, capping, or vapor intrusion liner).
Institutional Control (ITRC)
  A legal or administrative restriction on the use of, or access to a site or facility to eliminate or minimize potential exposure to chemicals of concern (such as proprietary controls or governmental controls).
  https://institutionalcontrols.itrcweb.org/glossary/

## Slide 7
Temporary Storage
~ 1 year

## Slide 8
Drilling Waste Burial Pit – Long Term Storage
Forever

## Slide 9
Drilling Waste Burial Pit
ITRC. 2012. Incremental Sampling Methodology.
https://www.itrcweb.org/ism-1/3_1_2_Conceptual_Site_Models.html

## Slide 10
Geosynthetic Institute

## Slide 11
Geosynthetic Institute
Degradation Mechanisms
  UV Light, Oxidation, Ozone, Hydrolysis, Chemical, Radioactivity, Biological, Stress State, Temperature
Lifetime Stages
  Stage A - Antioxidant Depletion Time
  Stage B - Induction Time to the Onset of Degradation
  Stage C - Time to Reach 50% Degradation (i.e., the Halflife)
  (Koerner, et al. 2011.)

## Slide 12
Geosynthetic Institute
(Koerner et al. 2011.)

## Slide 13
Geosynthetic Institute
(Koerner et al. 2011.)

## Slide 14
Typical Controls at a Landfill Site
ITRC. 2006. Evaluating, Optimizing, or Ending Post-Closure Care at Municipal Solid Waste Landfills Based on Site-Specific Data Evaluations

## Slide 15
Drilling Waste Burial Pit

## Slide 16
Concerns
Geosynthetics will degrade over time according to literature
Some contaminants may degrade over time, but may generate other COCs (metabolites)
Some contaminants will not degrade (salts, heavy metals)
There are typically no long term institutional controls in place at burial sites
Potential for contaminants to migrate from the burial site over long periods of time

## Slide 17
Wrap Up
About Scott Energy
Professional Engineering Firm
Oilfield Service Company
Experts in E&P waste management
Sustainable practices based solely on sound science
Questions?