## Slide 1
Drone Magnetometry Applied to Detecting and Mapping Legacy Wells and Pipelines
Ronald S. Bell
Geophysicist & geoDRONEologist
25th International Petroleum Environmental Conference
Presented at the:
Presented on: October 30, 2018 - Grand Hyatt Denver Hotel Denver, CO

## Slide 2
Geoscientific mapping by drone
Benefits
Limitations & Restrictions
Drone Mapping workflow
A Three Part Presentation
What we can do today!
The Magnetic Method
The MagArrowTM
Locating abandoned well
Locating a pipeline
EM surveys for pipelines
PART 1
PART 2
PART 3
UAV Flight Services team preparing for drone enabled magnetic survey at and elevation of 12,400 ft

## Slide 3
Geoscientific mapping by drone
Color Photographs
Near Infrared
Short Wave Infrared
Thermal Infrared
Magnetic
vegetation stress (NVDI)
soil and rock type \ alteration zones
groundwater seeps
thermal emissions \ extractive process management
contaminant detection & delineation
gaseous emissions
rock type / alteration zones
geologic structural
buried objects & UXO
infrastructure detection and delineation
contaminant detection and delineation
LiDAR
Multi- / hyper- spectral
ground surface
up-to-date, high definition color photomosaic base map
digital elevation model / digital surface model
biological species ID and inventory
asset management / project work flow / security
high definition photo-geological mapping
subsurface
ElectroMagnetic (EM)
Color Video (4K)
elevation point clouds / 3D surfaces
digital elevation model / digital surface model
Gamma Ray Spectrometry
geological mapping
hazard detection
geophysics
remote sensing
Visible Light

## Slide 4
Benefits
obtain “Bird’s Eye” view
higher definition data
lower cost per data point
less time to acquire
access difficult to reach areas
multiple data types
enhances safety of field staff
reduces risk of property damage
low altitude equals more signal
facilitates temporal change detection
fault

## Slide 5
Limitations
weather
vertical structures i.e. trees
short duration flights
small payload (typically < 3 kg)
aircraft flight characteristics
maximum flight altitude: 400 feet AGL
visual line of sight (VLOS)
day time operations only
no operations over people
one operator = one UAS
certified unmanned aircraft pilot
Restrictions

## Slide 6
Mapping by Drone – the workflow
2 - Plan, Permit,
& Schedule Mission
4- Deliver Data
& Information
1 - Select Area of Interest
3 – Data
Collect
UAV flight path on DEM
Color orthophoto on 3D DEM

## Slide 7: The Magnetic Method
The earth's magnetic field induces magnetization in the rock and buried objects.
Magnetic signature due to the induced magnetization, I, is a function of the direction and intensity of the geomagnetic field.
The intrinsic magnetic susceptibility, k, of the rock or object material controls the degree to which it will be magnetized: I = kT T= inducing field
The size, shape, and orientation of the buried object or rock formation within the inducing magnetic field determines the characteristic anomaly shape.
Objects made of a high magnetic susceptibility material, i.e. steel or iron, will result in significant magnetic anomalies.

## Slide 8: Magnetic Survey
Modern magnetometers consist a high sensitivity, high sample rate magnetic field sensor paired with a digital recording data logger and global positioning system (GPS).
GPS
Antenna
Magnetic Field Sensor
Control Unit \ data logger
The resolving power of the magnetic method is a function of the proximity of the magnetic field sensor to the source of the magnetic field anomaly and the spatial density of the magnetic field measurements.
The objective of a magnetic survey is to map the spatial and temporal variations in the earth’s magnetic field.
Thus, a magnetic survey can be accomplished by a human being walking over the ground surface or by a vehicle of some type. (i.e. airplane, boat, ATV, etc. ). Autonomous operated unmanned aerial vehicles (UAV) extend the effective range of a human being while simultaneously collecting higher resolution data in about 20% of the time.

## Slide 9
MagArrowTM – a drone enabled magnetometer
MagArrowTM
Power: 2.5 W per sensor
Weight: less that 2 lbs.

## Slide 10
What is a plugged and abandoned O&G well?
ground surface
~10 ft bgs
~30 ft bgs
~5000 ft bgs
steel casing
steel pipe
A vertically oriented cylinder made of steel extending into the subsurface.
Typically, the top segment has been cut off ~10 ft below the ground surface.

## Slide 11
What is the magnetic signature of a well?
Martinek, B.C., Ground Based Magnetometer Survey of Abandoned Wells at the Rocky Mountain Arsenal, A Case History, (1984), M-TR43, Geometrics, Inc., San Jose , CA
available for download at www.geometrics.com
If the well is vertical and shallow, the magnetic signature will a monopole response in profile and a uniquely characteristic circular contour pattern
As the depth to the well increase, the signature will grade into a dipolar response but maintain a circular pattern in contour.

## Slide 12
What is the magnetic signature of a pipeline?
ground surface
buried ~ 5 to 10 ft bgs
steel pipe segments
A typical pipeline is made up of lengths of individual pipe welded together. The magnetic signature is a series of dipolar anomalies along a linear trend.
The response is complicated by variations in the magnetic susceptibility of the steel used in the manufacture of the pipe, the remanent magnetization of the pipe, and the changes in the intrinsic magnetization due to the welding of the segments of pipe together.

## Slide 13
What does a P&A O&G well site look like?
Google Earth Image
Looking west from point A
Point A

## Slide 14
Traditional method for locating a well
Query database maintained by the state to obtain information about well
Hire a professional land surveyor to survey in the location based on the description and/or longitude & latitude coordinates listed in the database
Contract with local firm to dig on location marked by land surveyor to verify location.

## Slide 15
Does the “Traditional Method” work?
Yes, but often the “searching by digging” can be quite expensive if the well is poorly located.
P&A oil well located using the “search by digging” method.
flow pipe

## Slide 16
Drone Enabled Magnetic Survey
MagArrowTM
# flights: 1
time: 15 minutes
UAV altitude: 15 m agl
sensor height: 11.6 m

## Slide 17
Drone Enabled Magnetic Survey
location from longitude latitude coordinates extracted from COGCC database

## Slide 18
Pipeline Mapping Survey
Total Magnetic
Intensity

## Slide 19
MagHeatTM
Pipeline Mapping Survey

## Slide 20
located pipelines
located
P&A wells
Pipeline Mapping Survey

## Slide 21
Factors impacting the success of a drone enabled magnetic survey for locating wells and pipelines.
Line Spacing
Sensor Altitude
Aircraft Speed
Weather
Site Accessibility
Well Construction
Non-vertical well
Casing & pipe integrity
Buried pipe and debris

## Slide 22
Electromagnetic (EM) Induction Conductivity Meter
CMD Explorer
frequency domain - coplanar loop-loop system
3 coil separations + 2 coil orientations = 6 depths of investigation
vertical magnetic dipole (VMD): 2.2, 4.2, & 6.7 m
horizontal magnetic dipole (HMD): 1.1, 2.1, & 3.3 m
GPS Receiver
Data Logger \ Control Unit
16 feet

## Slide 23
EM Cond 1
EM Cond 2
EM Cond 3
EM Conductivity – multiple depths of investigation
~ 1 m
~ 2 m
~ 3 m
buried pipeline
possible contaminated area

## Slide 24
EM COND 3 Profiles
on MagHeatTM
color contours
The disappearing EM anomaly is the result of a break in the electrical conductor ( i.e. pipeline).
The MagHeatTM data indicates the presence of ferromagnetic objects in the subsurface.
Conclusion:
The pipeline was severed and left in place.

## Slide 25
What we can do today!
Drone magnetometry to precisely locate P&A oil and gas wells.
Drone magnetometry to detect and delineate legacy steel pipelines.
Ground EM to locate metal (e.g. pipelines, etc.) and characterize the subsurface to detect and delineate pipeline leaks, salt scars, and other contamination.

## Slide 26
Acknowledgements
Geophysical Instruments
http://juniperunmanned.com/
http://geometrics.com/
UAS Flight Services and Data Analytics
We gratefully thank the following companies for their assistance and support in the acquistion of the drone enabled magnetic data.

## Slide 27
Thank you.
Questions?
mobile: 720-220-3596
IGS office: 303-462-1466
e-mail: rbell@igsdenver.com
Ronald S. Bell
For more information, contact:
Senior Geophysicist & geoDRONEologist
Collier Consulting office: 720-487-9200
e-mail: ron@collierconsulting.com
http://collierconsulting.com/
Collier Consulting Inc.
590 E. South Loop
Stephenville, TX 76401