## Slide 1: j
Ecosystem Service Response to Interim Reclamation on Oil and Gas Well Pads in Wyoming
Michael Curran abc and Dr. Peter Stahl abc
a- Department of Ecosystem Science and Management, University of Wyoming
b- Program in Ecology, University of Wyoming
c- Wyoming Reclamation and Restoration Center

## Slide 2: Reclamation as a process

## Slide 3: Land Reclamation and Ecosystem Restoration in Oil and Gas Fields
May be viewed as ‘assisted succession’ (McCann 2007, Walker et al. 2007)
Typically focused on structural, not functional, end points
  Regulatory Criteria – Roll Over/Bond Release
    Lack of attention on native annual forbs (Prasser 2015)
    Difficult (species dependent) to obtain commercial seed mixes (Curran et al. 2015)
    Vary among agencies and on private land
  Reclaimed sites compared to adjacent, undisturbed cultural reference sites (BLM Gold Book 2007)

## Slide 4: Ecosystem services as ‘functional end points’
Soil Recovery
  Accumulate, stablize and store carbon
  Prevent erosion
Vegetation
  NPP
  Cover/diversity
Insect abundance/diversity
  Used as indicators of reclamation success in the past
  Most work done with pollinators in crop systems

## Slide 5: Challenges of restoring a ‘cold desert’
Arid/semi-arid environment
  Low, unpredictable precipitation
Cold climate
  Average <50 frost free days
Sagebrush steppe ecosystem
  Sagebrush often takes many years to reestablish
Soil conditions, environmental quality, erosion
  Stripping and stockpiling soil may introduce unsuitable growing medium to surface

## Slide 6
Wamsutter

## Slide 7: * Dr. Jay Norton (UWYO)

## Slide 8: *Dr. Jay Norton (UWYO)

## Slide 9: Conclusions? (* Dr. Jay Norton (UWYO))
Compared with degraded reference sites, reclaimed sites seem to recover or exceed original SOM levels within seven years;
  Possibly due to increased herbaceous vegetation
Potentially mineralizable carbon recovers more slowly;
  Possibly due to loss of soil structure, which protects labile SOM from mineralization, and continued accelerated mineralization, lack of woody species…
Interest in reclamation research is as variable as annual rainfall.

## Slide 10: Study Area (Vegetation and Insects)
Pinedale Anticline natural gas field (Pinedale, WY, USA)
  High daily and annual temperature fluctuations
  ~2,100 m elevation
  42 day frost-free period
  Low (254-356 mm) and unpredictable precipitation
Highly fragmented
  5,289 acres of initial disturbance with 3,668 acres undergoing active reclamation (69.3%)
Subject to domestic livestock grazing dating back to 1871
All sites selected in study fall in ESD R034AY222WY
  Historic climax plant community of mixed grass, big sage

## Slide 12: Vegetation Sampling Results
Beeplant reclaimed well pads
  19-33% bareground, 23-35% beeplant, 15-31% Russian thistle, <1% sagebrush, 17-23% herbaceous litter, <1% bunch grass, <1% rhizomatous grass)
Reference sites adjacent to beeplant pads
  43-59% bareground, 20-31% sagebrush, 3-9% herbaceous litter, 8-14% woody litter, 1-5% bunch grass, 0-2% rhizomatous grass, 0% forbs
Native grass reclaimed well pads
  55-72% bareground, 0-6% sagebrush, 18-29% bunchgrass, 1-3% rhizomatous grass, <1% forbs, 2-10% herbaceous litter
Reference sites adjacent to native grass pads
  53-59% bareground, 17-27% sagebrush, 3-10% bunchgrass, 0-3% rhizomatous grass, 0% forbs, 0-6% herbaceous litter, 6-11% woody litter

## Slide 13: NPP/NDVI

## Slide 15: Ain b

## Slide 16: Insects and Ecosystem Services
Provisioning Services
  Food, raw materials, fresh water, medicinal resources
Regulating Services
  Local climate and air quality, carbon sequestration and storage, moderation of extreme events, waste-water treatment, erosion control/soil fertility, pollination, biological control
Habitat or Supporting Services
  Habitat for species (food, shelter, water), maintenance of genetic diversity (high species diversity often means high genetic diversity), nutrient cycling
Cultural Services
  Recreation (mental & physical health), tourism, aesthetic appreciation and inspiration for culture, art, and design, spiritual experience
www.teebweb.org

## Slide 17: Information about Insects from previous literature
Plant-vigor hypothesis (Price 1991)
Mass-flowering hypothesis (Westphal et al. 2003)
Many insects avoid terpenoids (produced by old sagebrush) and very few insect families eat wood
Not many studies have been conducted to see how grazing impacts insects, but most show negative impact (Fleischer 1994)
Not much is known about wild pollinators in rangelands (Harmon 2011)

## Slide 18: Hypotheses
Insect abundance and family richness (2015 and 2016) would be higher on reclaimed well pads with mass-flowering Rocky Mountain beeplant than on reference sites adjacent to them (mass-flowering hypothesis)
Insect abundance and family richness (2015 and 2016) would be higher on reclaimed well pads with native grasses than on reference sites adjacent to them (plant-vigor hypothesis, insect avoidance to terpenoids)
Insect abundance and family richness (2015 and 2016) would be different on RMBP reclaimed sites and native grass reclaimed sites
Insect abundance and family richness (2015 and 2016) would be different on reference sites adjacent to RMBP reclaimed sites and reference sites adjacent to native grass reclaimed sites

## Slide 19: Vegetation Sampling Methods
In 2015 and 2016, 40m transects were placed parallel to edge of well pads at distances of 5m and 10m away from the edge on both reclaimed and reference sites.
0.5m2 NADIR images were taken every 5 meters along the transect (9 images per transect) using methods consistent with Cagney et al. 2011
  40 points within each image were processed using SamplePoint (Booth 2006) software

## Slide 20: Insect Abundance

## Slide 21: Insect Family Richness

## Slide 22: 2015 Whittaker Plot

## Slide 23: 2015 Ecological Role

## Slide 24: 2016 Whittaker Plot

## Slide 25: 2016 Ecological Role

## Slide 26: Discussion
In all cases, more insects found on reclaimed sites than reference areas
More insect abundance and richness on reclaimed sites with RMBP than native grasses
More insect abundance and richness on reference areas adjacent to RMBP sites than reference sites adjacent to native grass sites

## Slide 27: Discussion
Rocky Mountain beeplant is known to perform well in disturbed environments (Cane 2008) and may be a useful tool in combating invasive weeds (Prasser 2015)
  Our study shows RMBP also may be a useful tool late in the season to attract pollinators and other insects
Few studies focusing on ecosystem services at early seral stages of reclaimed (drastically disturbed) lands in arid, high altitude environments
  Our study shows, at least in terms of insect diversity and abundance, some earlier stages of reclaimed sites are performing better than the ‘historic climax plant community’ or cultural reference sites
Reference site selection in a semi-natural system may be flawed
  Do we want to go to a decadent sagebrush sea with little understory in all cases? Patchiness and vegetation diversity on well pads may have some benefits

## Slide 28: Conclusions
First study to examine insects on reclaimed natural gas well pads
Informs future research regarding wild pollinators (and insects in general) in (high altitude/arid) rangelands
Informs wildlife conservation with more studies
  Forbs which attract insects are likely to be beneficial to birds which eat forbs and insects (Curran et al. 2015)
Our study seemingly confirms well-tested hypotheses conducted in other ecosystems
Should we be aiming to restore to a degraded system?
  Soil C/N seem to be accruing fast
  Insect and plant diversity increase

## Slide 29: Future Research: Other areas (Jonah), seasons (May, July, August) traps (sweeps and sticky) and monitoring (sticky and mark-capture)

## Slide 38: Acknowledgements
Calvin Strom (Assistant Director, WRRC)
Dr. Jay Norton (soil data)
Dr. Doug Smith (insect ID)
Dr. Taylor Crow (help in R)
Dr. David Legg & Dr. Tim Robinson (study design, statistical analysis)
QEP Resources & Anadarko Petroleum Company(field site access)
Jonah Energy, LLC (funding, field site access)