## Slide 1
GENERAL OVERVIEW OF PFAS
PER- AND POLYFLUOROALKYL SUBSTANCES
25th International Petroleum Environmental Conference November 1, 2018

## Slide 2: Today’s Topics
PFAS Naming Conventions
Physical/Chemical Properties of PFAS
Sources of PFAS and Potentially-affected Sites
AFFF
Sampling Issues and Quality Control
Regulatory
Treatment

## Slide 3: PFAS Naming Conventions

## Slide 4: Quick Chemistry Lesson #1
  Remember: PFAS are Per and Polyfluoroalkyl substances
C
F
F
F
F
F
C
C
F
F
F
C
C
F
F
F
F
C
C
F
F
F
C
SO3H
F
F
(PFOS)
SO3H = Head
PFAAs
  Perfluoroalkane sulfonates (or sulfonic acids): PFSAs
  Perfluoroalkane carboxylates (or carboxylic acids): PFCAs
  Per-fluoroalkyl substances: fully fluorinated alkyl tail
O
OH
C
F
F
F
F
F
F
F
F
F
F
F
F
(PFOA)
F
F
F
C
C
C
C
C
C
C
COOH = Head
Alkyl tail, fully fluorinated

## Slide 5: Quick Chemistry Lesson #2
  Remember: PFAS are Per and Polyfluoroalkyl substances
Fluorotelomer Alcohol (8:2 FTOH)
C
F
F
F
C
C
F
F
F
C
C
F
F
F
F
C
C
F
F
F
C
F
F
F
F
C
C
Non-fluorine atom on one or more carbons.
OH
  Poly-fluoroalkyl substances: non-fluorine atom (typically hydrogen or oxygen) attached to at least one carbon atom
Polyfluoroalkyl substances may also be degraded to perfluoroalkyl substances (e.g., PFOS or PFOA): PRECURSORS

## Slide 6: What Are PFAS?
  Poly- and per-fluoroalkyl substances
    Generic family of chemicals
    Manmade and do not occur naturally
    Used since 1940 (Critical for the Manhattan Project)
    Can be branched or unbranched
    Short chain or long chain
    Used to make products that resist heat, oils, grease, stains, and water
Most prevalent and researched: PFOA and PFOS

## Slide 7: Chemical Properties of Perfluoroalkyl Substances
C-F: Strong bond
Chemically and thermally stable
Water soluble and mobile in groundwater
Surfactant properties
Recalcitrant in environment
A PFAS Micelle

## Slide 8: Sources of PFAS and Potentially Affected Sites

## Slide 9: Where Are PFAS Used?

## Slide 10: What Types of Sites Can Be Sources of PFAS?
Fire training facilities
Fire stations
Refineries
DoD sites/Military bases
Commercial and private airports
Landfills (leaching from consumer products)
Biosolids land application
Rail yards
Chemical facilities
Plating facilities
Textile/carpet manufacturers
Residential areas with septic systems

## Slide 11: Global Manufacture and Use of PFAS
PFAS Manufactured Globally
PFOA & PFOS No Longer Produced
Class B AFFF with PFAS Banned
Prohibits Import, Manufacture, Use & Sale of PFOS/PFOA
Banned Sale, Use and Import of PFOA
Restrict Manufacture, Import, Export, and Use of PFOS
Increased Production of PFOA
EtFOSA Produced on Industrial Scale

## Slide 12
  Aqueous Film Forming Foam (AFFF)
Notes: So, let’s get into the fire fighting foams that is of most interest to the fuel and petrochemical manufacturers.

## Slide 13: What is AFFF?
Highly effective fire-fighting foam
Used for hydrocarbon fuel fires
AFFF acts as:
  An aqueous foam: primary fire extinguishing agent
  An aqueous film former: a fuel vapor suppressor

## Slide 14: Where is AFFF Used?
Airports (military/domestic)
Petrochemical Facilities
Municipal Fire Dept.
Industrial Fixed Systems
Military / Government
Marine – Off Shore Fire Protection
Where:
  Historical Use (where used to fight a fire)
  Fire Training Areas
  Nozzle Testing Areas
  Storage Areas

## Slide 15: Types of Fluorine-Based AFFF
PFOS based (80%)
Telomer based (20%)
Developed in 1960s
Production ended in 2002
Inventory remains in many locations
Contain or breakdown to PFOS & PFHxS and possibly PFOA
Legacy 1st Generation AFFF
Sold from 1970s - 2016
Telomers
PFOR compounds (R= cationic and anionic heads) “precursors”
PFOR – transformation to sulfonates and carboxylates
Long-chain fluorotelomers (8:2 FTS) can breakdown to PFOA
2nd Generation Fluorotelomer & Precursors AFFF
Most foam mfrs transitioned to this
No PFOS and no breakdown to PFOS
Short-chain fluorotelomers (6:2 and 4:2 FTS)
May contain trace amts of PFOA and PFOA precursors
Considered lower in toxicity and reduced BAP
Modern Fluorotelomer AFFF
Notes: The original fluorinated AFFF was made with PFOS, by 3M. Of course others got into the business with other compounds. The fluorotelemers are these polyfluoro substances that can degrade to other perfluoro substances. Currently the fluorotelomer AFFF are using shorter chain polyfluoro substances. These changes in the types of AFFF can be used to fingerprint different sources of AFFF and to fingerprint multiple sources (e.g., separating a landfill PFAS from an AFFF PFAS source).

## Slide 16: Fluorine-Free Foams
Alternative to AFFF in some applications
Being used at some airports and industrial facilities in Europe, Australia, and other countries
Do not contain PFAS or other persistent chemicals
Contain hydrocarbon surfactants, solvents, and stabilizers
Fluorine-Free Foams available since early 1900s

## Slide 17: PFAS Sampling Issues and Quality Control

## Slide 18: How Do We Sample PFAS?
Similar to conventional sampling (e.g., low-flow techniques, direct push, etc.)
Special care required to prevent cross contamination
Use of and exclusion of specific sampling equipment and materials

## Slide 19: PFAS Sampling Dos and Don’ts

## Slide 20: PFAS Sampling Dos and Don’ts continued

## Slide 21: Other Special Considerations
Field QC
Decontamination of sampling equipment
No pre-wrapped food or snacks
Avoid cosmetics, moisturizers, hand creams on day of sampling.
Do not filter aqueous samples.
Visitors to site must remain at least 30 feet from sampling area.
Wash hands with water after leaving vehicle before setting up on a well.
Partitioning of PFAS to surface in wells and reservoirs

## Slide 22
  PFAS Fate and Transport
Notes: PFAS compounds are soluble in water, are not strongly adsorbed to soils, and have very low standards, and the Per fluourinated compounds are stable, not biodegradable. So, they are mobile in surface water and groundwater. But how mobile?

## Slide 23: PFAS Mobility
Other CVOC Plumes
BTEX Plumes
Chorinated Ethene Plumes
PFAS Plumes
Theses PFAS sites are owned by DoD and are mostly Airforce bases
Other CVOC Plumes
BTEX Plumes
Chorinated Ethene Plumes
Q
BTEX Plumes
BTEX Plumes
Chorinated Ethene Plumes
Notes: BTEX plumes are typically pretty small because of their biodegradation. Chlorinated VOC plumes can be much larger, extending out up to 10,000 ft. But for comparison, PFAS plumes can be much longer because they don’t degrade AND because the standard is so much lower. For CVOCs you’re looking at detection limits of say 1 ug/L, but for PFAS your detection limits are <0.07 ug/L.

## Slide 24
  PFAS Environmental Regulations
  What is Occurring? – What to Expect?
Notes: Let’s jump over to the regulatory programs. What is going on around the country, and what can you expect?

## Slide 25: PFAS: The Rapidly Changing Regulatory Landscape
State | Year | Type | Promulgated? | PFOA | PFOS | PFNA | Other PFAS | Gen-X
 |  |  |  | (µg/L) |  |  |  | 
Alaska (AK) | 2016 | GW | Y | 0.40 | 0.40 |  |  | 
Connecticut (CT) | 2016 | GW |  | 0.07 | 0.07 | 0.07 | Y | 
Colorado (CO) | 2017 | DW |  | 0.07 | 0.07 |  | Y | 
Delaware (DE) | 2016 | GW |  | 0.07 | 0.07 |  | N | 
 | 2016 | GW |  | 0.07 | 0.07 |  | Y | 
Iowa (IA) | 2016 | Protected GW | Y | 0.07 | 0.07 |  | N | 
 |  | Non-protected GW | Y | 0.7 | 1 |  | N | 
Maine (ME) | 2016 | DW |  | 0.07 | 0.07 |  | N | 
 | 2016 | GW |  | 0.13 | 0.56 |  | N | 
 | 2016 | RW |  | 0.05 | 1.2 |  | N | 
Michigan (MI) | 2015 | SW | Y | 0.42 | 0.011 |  | N | 
 | 2018 | GW | Y | 0.07 | 0.07 |  | N | 
Minnesota (MN) | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
 | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
 | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
Nevada (NV) | 2015 | DW |  | 0.667 | 0.667 |  | Y | 
New Hampshire (NH) | 2016 | GW | Y | 0.07 | 0.07 |  | N | 
New Jersey (NJ) | 2015 | GW | Y |  |  | 0.010 | N | 
 | 2017 | GW | P |  |  | 0.010 | N | 
 | 2017 | DW | P |  |  | 0.013 | N | 
 | 2017 | DW | Y | 0.014 |  |  | N | 
North Carolina (NC) | 2006 | GW | Y | 2 |  |  | N | 
 | 2017 | DW |  |  |  |  | N | 0.14
Oregon (OR) | 2011 | SW | Y | 24 | 300 | 1 | Y | 
Texas (TX) | 2017 | GW | Y | 0.29 | 0.56 | 0.29 | Y | 
Vermont (VT) | 2018 | DW/GW | Y | 0.02 | 0.02 | 0.02 | N | 
International:
Australia
Canada
Denmark
Germany
Italy
Netherlands
Sweden
UK
Residential soil and soil leaching standards exist also.
Follow ITRC for updates
https://pfas1.itrcweb.org/fact-sheets/
State | Year | Type | Promulgated? | PFOA | PFOS | PFNA | Other PFAS | Gen-X
 |  |  |  | (µg/L) |  |  |  | 
Alaska (AK) | 2016 | GW | Y | 0.40 | 0.40 |  |  | 
Connecticut (CT) | 2016 | GW |  | 0.07 | 0.07 | 0.07 | Y | 
Colorado (CO) | 2017 | DW |  | 0.07 | 0.07 |  | Y | 
Delaware (DE) | 2016 | GW |  | 0.07 | 0.07 |  | N | 
 | 2016 | GW |  | 0.07 | 0.07 |  | Y | 
Iowa (IA) | 2016 | Protected GW | Y | 0.07 | 0.07 |  | N | 
 |  | Non-protected GW | Y | 0.7 | 1 |  | N | 
Maine (ME) | 2016 | DW |  | 0.07 | 0.07 |  | N | 
 | 2016 | GW |  | 0.13 | 0.56 |  | N | 
 | 2016 | RW |  | 0.05 | 1.2 |  | N | 
Michigan (MI) | 2015 | SW | Y | 0.42 | 0.011 |  | N | 
 | 2018 | GW | Y | 0.07 | 0.07 |  | N | 
Minnesota (MN) | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
 | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
 | 2017 | GW |  | 0.035 | 0.027 |  | Y | 
Nevada (NV) | 2015 | DW |  | 0.667 | 0.667 |  | Y | 
New Hampshire (NH) | 2016 | GW | Y | 0.07 | 0.07 |  | N | 
New Jersey (NJ) | 2015 | GW | Y |  |  | 0.010 | N | 
 | 2017 | GW | P |  |  | 0.010 | N | 
 | 2017 | DW | P |  |  | 0.013 | N | 
 | 2017 | DW | Y | 0.014 |  |  | N | 
North Carolina (NC) | 2006 | GW | Y | 2 |  |  | N | 
 | 2017 | DW |  |  |  |  | N | 0.14
Oregon (OR) | 2011 | SW | Y | 24 | 300 | 1 | Y | 
Texas (TX) | 2017 | GW | Y | 0.29 | 0.56 | 0.29 | Y | 
Vermont (VT) | 2018 | DW/GW | Y | 0.02 | 0.02 | 0.02 | N | 
Notes: Here’s a short summary of state’s with PFAS standards. Note the dates of these standards – 2015, 2016, through 2018. They’re all very recent. For example, look at Mich – their drinking water and gw remediation standards are 0.07 ug/L. Here in Texas, the standards are quite a bit higher, at 0.25 ug/L. These are both really low compared to the typical CVOC standards of 5 ug/L.
An easy way of keeping track of changes in state standards is through the ITRC guidance documents for PFAS.

## Slide 26: PFAS: The Rapidly Changing Regulatory Landscape
Examples over the last several months
Congress (Oct. 2, 2018) passed a bill to allow discontinuation of PFAS in airport fire fighting foams
EPA PFAS Summit – May 2018
  Initiate steps to evaluate need for MCLs
  Groundwater cleanup standards by fall of 2018
  Liability under CERCLA – PFOS/PFOA as haz. substances
  Held 5 PFAS listening sessions around the country (NH, PA, CO, NC, KS)
Michigan: Since the end of 2017 MI DEQ has:
  Set standards for:
    Drinking water and Groundwater Remediation
    WWTP discharge standards
    Air emission standards
  Required all POTWs to evaluate their industrial influents as PFAS sources
New Hampshire has required all landfill groundwater monitoring programs to analyze for PFAS
Community Action Groups analyzing for PFAS (e.g., A New York Landfill expansion permit)
Notes: The regulatory landscape is rapidly changing. For example: just this month, congress passed a bill to allow discontinuation of PFAS in airport AFFF.
Mr. Pruitt hosted an EPA PFAS summit meeting in May 2018, in which he committed EPA to:
Start evaluating whether
NYSDEC environmental sites sampling for PFAS, PFOA and PFOS are now on the hazardous substance list, and fire fighting foams that contain PFOA or PFOS are prohibited
Colonie LF opposition group collected nearby surface water samples, detecting PFOA in stormwater (68 ppt), in seeps near the Mohawk River (519 ppt), and in samples from the River (1-3 ppt)
California potentially identifying carpets with PFAS as “priority products” with special requirements.
Wisconsin has soil standards for PFOA and PFOS, but no groundwater standards yet.

## Slide 27
  PFAS Environmental Regulations
  How to Manage?

## Slide 28: PFAS – Sampling and Analysis When, Where, What, Why and How?
AFFF Inventory
Change out legacy AFFF
Develop SOPs for cleanup after use of AFFF
Inventory of historical use, training, storage & testing sites
Assess potential sensitive receptors
Review state inventories
Know where your PFAS-use sites are and their risk.
  With respect to water supplies – especially those with PFAS
  Adjacent surface water bodies
Notes: Know where your PFAS use sites are located. You’re bound for surprises if you don’t know where are how you’ve used these compounds. Does this a records search? Done under Attorney privilege? You can prioritize actions on sites until you know what you have.
PFAS Analytical methods:
Analysis of PFCs can be limited to just the two with standards or include a wider range of PFCs. The value of including a wider range is to fingerprint the source of PFCs.
    Potential for precursors?
    State requirements?
    Other PFAS for forensics?
Data validation can be critical – examples: a private well with a positive VC dete
Sampling protocols, especially for PFCS need to consider things as sub

## Slide 29: PFAS Remediation Alternatives - Water
In Situ Technologies
Emerging(?) technologies:
  Carbon injection
    PRB or Source Area
  Electro-Chemical Oxidation
  ART In-Well Circulation System
Low Volatility (rules out stripping)
Moderate solubility
Strength of C-F Bond
Treatment efficiency must be very high because of low (ppt) remediation objectives
Fate and Transport/ Remediation Challenges
Ex-Situ Technologies
Sorption/Ion Exchange
  Carbon (can be effective for some PFAS, but can be inefficient)
  Ion Exchange Resins (costly)
Emerging technologies:
  Reverse Osmosis
  Membrane filtration
  Thermal Treatment
  SAFF – Surface Activation Foam Fractionation
Notes: Now unfortunately, we don’t have a lot to say about remediation of PFAS in soil, groundwater or surface water. Currently the predominant response is removal and treatment – soil excavation and disposal, or groundwater extraction and treatment. There’s a lot to be discussed on what the best carbon treatment method should be used for groundwater treatment, but its still a pump and treat. There are some emerging technologies, for instance discussed at the Battelle conference in April. There’s a carbon injection method that can potentially sequester the PFAS, and there’s a electro-chemical oxidation technology that has positive bench scale studies that can destroy PFAS.

## Slide 30: Plug for ITRC PFAS Team
Includes >350 members: industry, academia, DOD, regulatory, consulting, analytical labs and vendors
Seven PFAS Fact Sheets:
  AFFF Introduction
  History and Use
  Naming Conventions and Chemical Properties
  Regulations and Guidance
  Fate and Transport
  Site Characterization, Sampling, Lab Methods
  Remediation Technologies and Methods
2018 – Technical Guidance Document

## Slide 31
Elizabeth Denly, ASQ CMQ/OE
P: (978) 656-3577 | E: EDenly@trcsolutions.com
www.trcsolutions.com
Acknowledgements:
Ken Quinn, TRC Technical Director
Mike Eberle, TRC Program Manager