## Slide 1
Cost-Effective In-Situ Remediation Biostimulation as a Residual Source Mass Remediation Strategy
Kent C. Armstrong, President
TerraStryke Products, LLC
284 Depot Street / P.O. Box 254
Andover, New Hampshire USA
—————————-
950 Fennell Avenue, Suite 105
Hamilton, Ontario CDN
L8V 1X2

## Slide 2
  Minimal Site Impacts Maximum Performance Cost-Effective Remediation
What is Biostimulation
  Provision of a microbial food or source of respiration i.e. ‘breathing’
  Goal is to enhance native microbial populations to sustainably destroy contaminants with minimal impact
What is Contamination
  Excessive source of food or respiratory support
  Petroleum Hydrocarbons are food (Carbon C+)
  Chlorinated Solvents represent sources of respiration (electrons Cl-)

## Slide 3
  TPHenhanced™
  Biostimulation additive
  Includes alternative respiratory sources (electron acceptors)
  i.e. does not contain oxygen (O2)
  Contains proprietary blend of macro-micro nutrients
  Patent-Pending formulation which assists all stakeholders chance to:
  realize contaminant destruction under anaerobic conditions
  eliminate long-term above-ground equipment
  maximize smear zone destruction
  expedited solubilization (flux) of residual source mass

## Slide 4
  TPHenhanced™
  Application: Petroleum Hydrocarbon Contaminants (PHCs)
  PHCs - GRO/DRO, JP Fuel, Stoddard Oil, MEK
  BTEX Contaminants
  MtBE
  Carbon tetrachloride
  Compound Benzene Contaminants
  chlorobenzenes
  trimethyl benzene

## Slide 5
  Massive influx of Carbon
  Oxidant load ‘scavenges’ available respiratory sources
  Causes geochemistry in impacted area to become reducing
  Drives groundwater geochemistry anaerobic, even methanogenic
  Conditions which limit microbial populations ability to ‘breathe’
Specifically, PHCs

## Slide 6
PHCs also bring with them
    smear zone, residual source mass concerns
    Rebound
    Vapors, indoor ambient air concerns, even LEL issues
  Sorbed and/or gangliatic (‘bleb’) contaminant mass not available to microbes
  Traditionally, we re-supply respiratory source using Oxygen (O2)
  Limited in terms of loading capacity and length of availability
  O2 has a limited ‘effect-residency time’
Petroleum Hydrocarbon Contamination (PHCs)

## Slide 7
  Provides respiratory support
  Replaces scavenged respiratory sources (electrons)
  Drives groundwater geochemistry out of methanogenesis
  Keeps treatment zone anaerobic, leveraging existing conditions
  Proprietary, patent-pending Macro-Micro nutrient forlulation
  Enhances growth and ‘fitness’ of native microbial communities
PHC Remediation using TPHenhanced™

## Slide 8
  Initial decrease in dissolved-phase groundwater concentrations
  Increase in microbial densities
  If residual mass is present
    increase in [dissolved-phase] = expedited residual mass solubilization
    due to natural biosurfactant production
    allows greater microbial performance and communications
    eliminates rebound up-front
  Superior dissolve phase destruction – long-term site compliance
What will we observe?

## Slide 9
  Legacy upstream oil-gas production site
  Treatment zone = footprint of former produce water pond
  Dissolved-phase and residual source mass BTEX constituents primary contaminants-of-concern
  BTEX contaminants-of-concern
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 10
  June 2014 Initial Remedial Action
  Source removal excavated ≈400 c.y.
  Vacuum truck removed ≈65 barrels impacted gw
  [BTEX] on excavation floor remained above standards
  Carbon ‘trap-and-linger’ product applied (≈100 lbs)
    Addressed initial dissolve-phase contaminant issue
    Unable to address rebound
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 11
  Network of 25 monitoring wells installed Fall 2014
  June 2015 monitoring results indicate [BTEX] remain above remediation objectives (Benzene 5.0 ug/L)
  2015 Carbon based deployment repeated
  using >5,000 pounds
  Secondary treatment included persulfate injections
  4-events
  26 injection locations
  using >3,500 pounds per event
  >14,000 pounds persulfate
  Cha-ching………..
  Results – continued rebound and asymptotic [BTEX] exceedances
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 12
  2017 Amended treatment zone with TPHenhanced™
  Used Passive Release Sock (PRS) deployment units
  Utilized existing 26 ‘injection’ node network
    50 lbs additive over 5,600 square foot area
  Three replacement events over 9-month period
  Total additive volume approaches 150-pounds
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 13
Ground surface
Groundwater Flow Direction
Area of Influence
Reproducible, not scalable
Not for compliance testing
PRS Pilot Study Schematic
Monitoring Program
Baseline
Each replacement event
Non-purge
Low-flow
6-8 replacement events typical

Additive filled Passive Release Sock (PRS)
Deployed into existing 2-inch gw monitoring well
Passively amend saturated screened interval
Create 3-5 foot area-of-influence
Replace PRS units every 10-14 days
Typically 5-8 replacement events

## Slide 14
Indicator Metrics
Field Parameters
ORP, DO, pH, Temperature
Geochemistry
Nitrates (NO3)
Diss. Iron/Manganese (Fe/Mn)
Sulphates (SO4)
Ethane/Methane/Ethene (MEE) - optional
Chloride (Cl-) - cVOC sites only
Analytical
Contaminant of Concern (EPA 8260)
PRS Pilot Study Groundwater Monitoring Metrics
Additive efficacy is determined by comparing baseline data to performance data results
Analysis for bacterial populations is also recommended

## Slide 15
  Results: MW-4 (downgradient)
    84%↓ reduction realized in <4 months; then,
    >1,000%↑ increased (solubilization); followed by,
    >98%↓ [Benzene] 5-months later…….
    >83%↓ Ethyl-benzene
    >97%↓ Xylenes
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 16
  2017 Amended treatment zone with TPHenhanced™
  Used Passive Release Sock (PRS) deployment units
  Utilized existing 26 ‘injection’ node network
    50 lbs additive over 5,600 square foot area
  Three replacement events over 9-month period
  Total additive volume approaches 150-pounds
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 17
Chart: MW-04
| 42810 | 42853 | 42892 | 42912 | 42955 | 43088
Total [BTEX] ug/L | 2389 | 378 | 1400 | 4395 | 190
[Nitrate] mg/L | 0.05 | 3.02 | 0.462 | 0.5
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond
MW-04 downgradient, residual mass present
Initially dissolved-phase reductions as additive availability increases
Additive exhausted as mass solubilized
Reductions continued without additive

## Slide 18
Chart: MW-07
| 42810 | 42853 | 42892 | 42912 | 42955 | 43088
Total [BTEX] ug/L | 10615 | 2221 | 3142 | 8765 | 14100
[Nitrate] mg/L | 0.05 | 17.6 | 0.5 | 0.5
MW-07 within retention pond
Significant residual mass present
Dissolved-phase reductions with availability
Additive exhausted as mass solubilized
[BTEX] increase without additive
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 19
  2018
  Both MW-4 and MW-7 [BTEX] reached BDL
  Slight rebound occurring at MW-7 within pond area
  Residual mass remains
  Second PRS deployment event initiated October 2018
  Utilizing same 26 ‘injection’ node network
    ≈50 lbs additive over 5,600 square foot area per event
  Three replacement events over 9-month period
  Total additive cost to date < $20,000.00
  Treatment cost approaching $15 per treated ton
TPHenhanced™ - Petroleum Case Study
Upstream Production-Water Collection Pond

## Slide 20
Maine DEP
Searsport Pipeline Argyle Pump Station
TPHENHANCED™
Chart: 
| June 7 2011 | 5-Jul-11 | 20-Jul-11 | 8-Aug-11 | 25-Aug-11 | 7-Sep-11 | 21-Sep-11 | 28-Oct-11
Amendment mg/L | 0 | 1400 | 7000 | 64 | 67 | 2000 | 1500 | 230
Total TPH µg/L | 7549 | 9387 | 8209 | 3026 | 7479 | 4209 | 4124 | 226
Increase Additive Availability
Enhance Microbial Respiration
Expedite Dissolve Phase Contaminant Assimilation
Exhaust Additive Availability
Return to Methanogenic Conditions; No Biotic Activity
Rebound
More Additive
Increased microbial activity
Realize 97% Reduction [PHC] =Passive Aggressive Destruction
Observations

## Slide 21
Chart: Δ [VOCtotal] Solid Phase
| Microcosm 1 | Microcosm 2 | Microcosm 3 | Control
Day 1 | 10500 | 10500 | 10500 | 10500
Day 20 | 4250 | 5500 | 3500 | 5750
Day 47 | 400 | 5250 | 500 | 9250
Aerobic
Anaerobic
TPHenhanced
Control
Microcosm Study Comparing Various Aerobic/Anaerobic Strategies

## Slide 22
Microcosm Study Comparing Various Aerobic/Anaerobic Strategies
Aerobic
Anaerobic
TPHenhanced
Control
BioNutrient100
Realize twice the microbial growth
Achieves population thresholds
Greater Bulk Fraction of Degrader Community

## Slide 23: Proof of Concept Evaluation ‘Drum Test’ Former Chanute USAFB Fire Training Area
[PHCs] in TPHenhanced® amended drum
    Decreased > 99% in 8-9 weeks
    With Greater Molar Destruction
Consultant Amended each Drum According to Vendors Instructions
  Drum 1 - TPHenhanced® by TerraStryke
Drum 2 - Oxygen Release Agent
Drum 3 – Control
Dosing Rate Equal to that Established for Full Scale Deployment

## Slide 24: Drum Study – Results Former Chanute USAFB Fire Training Area
TPHenhanced® | April 4 (μg/L) | April 18 (μg/L) | May 2 (μg/L) | May 21 (μg/L) | %Reduction
Benzene | 606 | 1,780 | 8,350 | 24.6 | 99.7%
Naphthalene | 197 | 178 | 302 | 2.02 | 99.3%
Toluene | 2,360 | 3,620 | 8,370 | 13.4 | 99.8%
1,2,4-TMB | 282 | 224 | 843 | 4.13 | 99.5%
pH | NT | 5.7 | 5.3 | 6.1 | NA
Oxygen Based | April 4 (μg/L) | April 18 (μg/L) | May 2 (μg/L) | May 21 (μg/L) | %Reduction
Benzene | 1,970 | 471 | 362 | 241 | 87.8%
Naphthalene | 213 | 76.7 | 34.1 | 8.36 | 96.1%
Toluene | 6,320 | 1,130 | 651 | 385 | 93.9%
1,2,4-TMB | 349 | 80.7 | 37.8 | 17.1 | 95.1%
pH | NT | 9.4 | 9.8 | 10.3 | 11.0

## Slide 25
Chart: 
| April 4 2012 | April 18 2012 | May 2 2012 | May 21 2012 | June 7 2012
TPHenhanced | 606 | 1780 | 8360 | 25 | 92
ORC-Advanced | 1970 | 471 | 362 | 241 | 20
TPHenhanced based [PHC] µg/L
TPHenhanced® vs. Oxygen
USAF [Benzene] Drum-Test Data
>9x the molar mass Benzene destroyed
Dissolve Phase Destruction
No Solubilization
Enhance Long-Term Compliance
Enhanced Biotic Degradation
> 99.7% destruction of solubilized mass
Enhanced Solubilization

## Slide 26
  Majority of PHC impacted groundwater plumes are anaerobic & chemically reducing
    We maintain existing geochemical conditions rather than try and ‘turn the Titanic’
    Reduce the amount of inertia needed to overcome
    Allows more energy for microbial populations to grow, ‘breathe’ and eat
    Projects typically incur lower effort, less impact, less costs
    E.g. aqueous solubility of TPHenhanced™ is ≥ 3 orders-of-magnitude other additives
  Greater loading ability helps diffusion propagate additive-slurry further into GW system
  Enhances additive distribution over and above advection for additive-slurry transport
  Particularly important in ‘tight’ less hydraulically conducive zones
Important TPHenhanced™ Talking Points

## Slide 27
  TPHenhanced™
  Will facilitate the realization of dissolved-phase and residual mass contaminant destruction
  Will maintain anaerobic conditions
  Will eliminate long-term above-ground equipment, nuisance noise, vapors, & emissions
  Will increase the bulk fraction of petroleum degraders
  Will expedite the microbial solubilization (flux) of residual source mass
  Will expedite smear zone contaminant destruction
  Is a Sustainable, Long-Term Solution for Site contaminant destruction
  TPHenhanced™ minimizes site impacts, reduces overall remediation costs, and represents the next generation of on-site remediation strategies using biostimulation
In Summary

## Slide 28
TerraStryke Products, LLC
P.O. Box 254, Andover NH
www.terrastryke.com
603.731.3159 karmstrong@terrastryke.com
QUESTIONS??

## Slide 29
Chart: MW-6
| 42718 | 42822 | 42915 | 43004 | 43087 | 43090 | 43104 | 43111 | 43125 | 43132 | 43139 | 43168 | 43202 | 43209 | 43216 | 43223
ORP | -159.9 | -109.7 | -163.9 | -110.8 | -140.3 | -21.1 | 8.2 | -40.7 | 39.8 | 56.9 | 77.6 | 32.6 | 75.3 | 86.9 | 310
[Nitrate] | 0.1 | 0.73 | 0.1 | 8.4 | 7.4 | 0.1 | 0.1 | 861 | 445 | 1.5
[BTEX] | 0.581 | 0.671 | 0.199 | 0.032 | 0.93 | 2.13 | 2.165 | 1.752 | 1.161 | 0.026 | 0.69 | 0.188 | 0.017
TPHenhanced™ - Petroleum Case Study
Former Service Station – Current Day Care Facility
Site former Service Station, now active Day Care
Under-ground USTs removed many years back
Long-term groundwater issues remain
Historical data indicates very low ORP
    indicative of methanogenic conditions
No respiratory sources available [NO3] BDL

## Slide 30
PHC dissolved-phase and residual mass
4-month evaluation period
        Dec 2017 – March 2018
Minimal additive deployed using PRS deployment units filled w/ TPHenhanced
2nd PRS deployment event April 2018
Benzene = contaminant of concern
>99% reduction in Benzene from peak bioavailability in <4 month period
TPHenhanced™ - Petroleum Case Study
Former Service Station – Current Day Care

## Slide 31
Period One: positive response w/regards to ORP as additive availability increases
Period Two: additive availability begins steady decline as availability is diminishing; ORP continues to climb out from methanogenesis
Period Three: additive availability declines sharply, and over time, ORP declines too
Period Four: new additive deployment increases availability sharply; and, ORP responds renewing favourable conditions
Note additive utilization is much quicker since microbial populations have increased; more folks needing to breathe!
TPHenhanced™ - Petroleum Case Study
Former Service Station – Current Day Care Facility
Chart: 
| 43081 | 43097 | 43111 | 43125 | 43139 | 43202 | 43209 | 43216 | 43223
Nitrate | 0.01 | 0.73 | 0.1 | 8.4 | 7.4 | 0.1 | 861 | 445 | 1.5
ORP | -140.3 | -40.7 | 39.8 | 32.6 | 57.3 | 86.9 | 310

## Slide 32
Chart: MW-06
| 43087 | 43097 | 43111 | 43125 | 43139 | 43202 | 43209 | 43216 | 43223
Nitrate | 0.01 | 0.73 | 0.1 | 8.4 | 7.4 | 0.1 | 861 | 445 | 1.5
[BTEX]total | 0.93 | 2.13 | 2.17 | 1.76 | 1.16 | 0.026 | 0.69 | 0.188 | 0.017
Additive availability increases
Significant increase in dissolved-phase concentration = enhanced solubilization
With additive available, assimilation of dissolved-phase PHCs outpaces solubilization
Additive availability parallels decreasing [PHCs]
Renewed additive availability, additional solubilization, subsequent destruction
>99% reduction in < 3-months
February 2018
TPHenhanced™ - Petroleum Case Study
Former Service Station – Current Day Care Facility

## Slide 33
Parker Colorado – Remedial Strategy - Approach
TPHenhanced® Biostimulation for 1,3,5-Trimethybenzene
Baseline groundwater sampling performed June 2015
[1,3,5-TMB] in groundwater ranged from:
474 micrograms per Liter (µg/L) at MW5 (source)
168 µg/L at MW-4 (proximate center)
195 µg/L MW7 (off-site)
Four rounds performance monitoring and sampling through June 2016.

## Slide 34
Treatability Evaluation Results September 2016
Parker Colorado – Bulk Tank Storage Facility
TPHenhanced® Biostimulation for 1,3,5-Trimethybenzene
Downgradient Location MW-7
  >99.5% Overall reduction [1,3,5-TMB]
Mid Location MW-4
  89.9% initial reduction
  Followed by 104% increase due to enhanced solubilization
  76.9% reduction overall
Source Location MW-5
  80.3% initial reduction
  Followed by 28.3% increase due to enhanced solubilization
  83.5% reduction from peak bioavailability

## Slide 35
Nitrate Reduction/Respiration
NO3-
(+5)
NO2-
(+3)
NO
(+2)
N2O
(+1)
N2
Manganese/Iron(III) Reduction/Respiration
Mn4+
Mn2+
Fe3+
Fe2+
Sulfate Reduction/Respiration
SO42-
H2S
C6H6
CO2
Ethene, Ethane, Methane Production
Presence of Free Cl-
Enhanced Reducing Conditions

## Slide 36
Aerobic Respiration
Nitrate Respiration
Sulphate Respiration
CO2 Respiration
Methanogenic Conditions
Iron – Manganese Respiration
O2 e- consumption complete
Anaerobic Conditions
Complete cVOC Biotransformation

## Slide 37
Nitrate Reduction/Respiration
NO3-
(+5)
NO2-
(+3)
NO
(+2)
N2O
(+1)
N2
Manganese/Iron(III) Reduction/Respiration
Mn4+
Mn2+
Fe3+
Fe2+
Sulfate Reduction/Respiration
SO42-
H2S
C6H6
CO2
Ethene, Ethane, Methane Production
Presence of Free Cl-
What In-Situ Amendment To Use??
Methanogenic Conditions
PHC, VOC, sVOC Contaminants
Little to No Biotic Activity
ORP
Provide Alternative Respiratory Pathways for Native Heterotrophic Microbial Populations
Enhance the Utilization of Naturally Occurring Respiratory Pathway Sources
Aerobic Conditions
Increase ORP
TPHenhanced™
Electron Donor
Alternative to O2 plus proprietary macro-micro nutrient formulation allowing respiration under anaerobic conditions
Low-Cost Low-Impact Safe Effective Sustainable