## Slide 1: Nuclear Magnetic Resonance Geophysical Investigations How to Quantify Aquifer Properties and Hydrocarbon Saturation Using Existing Monitoring Wells
Presented by: Brad Cross, ERM
October, 2018

## Slide 2: Goal: Closure of Contaminated Sites Problem: Heterogenaity vs Simplyfing Assumptions Solution: Resolve & understand the true aquifer fabric and multi-domain mass flux, mass storage systems
HRSC Tools
EC
CPT
Televiewers (acoustic/optic)
Heat-Pulse Flow Meter
HPT
MIP
LIF
Traditional Borehole Geophysics

## Slide 3: NMR builds on other HRSC tools:
Total porosity (no equivalent push-tool method)
Mobile & immobile pore volumes and pore size distribution (no equivalent push-tool method)
Hydraulic conductivity
Hydrocarbon (LNAPL) detection
Can be Acquired in Existing PVC-cased Wells

## Slide 4: Some Potential Applications:
High resolution conceptual site model development:
Perched water identification/residual (irreducible) water saturation
Aquifer mass flux and mass storage zones
Pore volume and pore size distribution characterization
Mass flux estimation
Quantification of changes in properties over time:
Infiltration, dewatering, residual saturation
Pore-space reduction (biofouling, subsidence)
Hydrocarbon (LNAPL) saturation reduction
Water supply/extraction well design/efficiency:
Optimize screen intervals
Assess redevelopment/rehabilitation

## Slide 5: NMR Measurement Physics
Properties of fluids that effect echo trains:
hydrogen index (HI)
longitudinal relaxation time (T1)
transverse relaxation time (T2)
diffusivity (D, the extent to which molecules move at random in the fluid).
T2 decay is proportional to pore size.
Porosity and pore size can be used to estimate permeability and the free fluid index (moveable fluids)

## Slide 6: Hydrologic Properties from NMR
  MRI directly measures the density of hydrogen nuclei in fluids
  Since density of hydrogen nuclei in water is known, data can be directly converted to an apparent water-filled porosity
  Can also determine the presence and quantities of different fluids

## Slide 7: Relaxation rates strongly correlate with pore size
T2 relaxation time increases with pore size

## Slide 8: Mobile versus Immobile Porosity
Using inverse modeling, composite echo trains are converted to porosity distributions.
Modeling is based on substantial laboratory calibrations to various soil/rock matrices
Mobile Fluid
Irreducible & Clay Bound Fluid
T2 cutoff

## Slide 9: Hydrologic Properties from NMR

## Slide 10: Multi-Phase Porosity Distribution

## Slide 11: Downhole NMR Logging
Used in oil & gas for decades
  Porosity, saturation, permeability
  Fluid-type oil/water (based on diffusion)
Oil field tools
  Operated by oil services companies
  Engineered for deep logging: high-P, high-T
  Very large: > 50 ft long & 5.75” diameter
  Very expensive: single well >$50,000

## Slide 12: Downhole NMR Logging

## Slide 13: Downhole NMR Logging

## Slide 14: Javelin System (VistaClara, Inc.)

## Slide 15: Javelin System (VistaClara, Inc.)
Can be deployed with Geoprobe Systems® equipment (direct-push tool)

## Slide 16: Straightforward Interpretation
Vertical resolution determined by length of coil in probe and pore size distribution
Processing automated in packaged software
Interpretation yields detailed characterization of aquifer structure and properties (bound/mobile water content, permeability)

## Slide 17: Case Study: Mill Tailings

## Slide 18: Mill Tailings Impoundment

## Slide 19: Hydrocarbon Detection Pilot Test Results

## Slide 20: Surface NMR

## Slide 21: Comparison of Logging and Surface NMR

## Slide 22: Summary
NMR is a viable technology for environmental and water supply practitioners
  Cost savings and reduced risk to human health and safety
  Improved site characterization and CSM refinement
  Strong potential to optimize remedial designs

## Slide 23: Thank you
  Brad Cross
Partner:
Pacific West
brad.cross@erm.com
+01 480 869 0604
Scottsdale, Arizona