## Slide 1: Pipeline Planning and Construction: Environmental Considerations
by Peter D. McKone, CWB (Weaver Consultants Group) and Caleb Watkins (Summit Midstream)
Notes: Jeff

## Slide 2: Outline
Regulatory Background
Permitting
Issues

## Slide 3: Waters of the U.S.

## Slide 4: Corps Regulatory Program
Protect navigation: Sections 9 and 10 of the Rivers and Harbors Act of 1899
Restore and maintain the physical, chemical and biological integrity of the nation's waters: Section 404 of the Clean Water Act
Protect marine resources associated with ocean disposal of dredged material: Section 103 of the Marine Protection, Research and Sanctuaries Act of 1972
Source: USACE Fort Worth District and Rapanos guidance

## Slide 5: Legal Background
USACE administers the regulatory aspects of dredge and fill activities.
EPA maintains ultimate responsibility for oversight of the USACE’s program.
Section 401 requires water quality certification from states.
Section 404 addresses permitting discharge of dredge and fill material.

## Slide 6: Types of Permits
Individual Permits
  Standard
  Letters of Permission
General Permits
  Regional
  Programmatic
  Nationwide

## Slide 7: Nationwide Permits
52 Nationwide Permits
Focus on environmental protection while providing timely and simplified authorizations for work in aquatic environments
Are valid for 5 years from date of issuance (effective 3/2017 to 3/2022)
Regional conditions
  Some statewide
  Some district specific

## Slide 8: Nationwide Permits (cont.)
Pre-Construction Notification (PCN) required in many cases
    Potential to impact cultural resources
    Potential to impact threatened or endangered species
    Presence of wetlands/special aquatic sites
Resource agency coordination required in some cases
If project meets scope & conditions of NWP & does not involve or exceed PCN triggers and/or thresholds, project may be completed w/o a written authorization
NOTE: If PCN required but not submitted & work initiated, activity is unauthorized

## Slide 9: NWP 12 Utility Line Activities
Construction, maintenance, repair, and removal of utility lines and associated facilities
Impacts limited to < 0.5 acres
Utility Lines
  No change in pre-construction contours
  Sidecasting limited to < 3 months
  Top 6-12” of trench should be backfilled with topsoil from the trench
  Cannot drain waters of the U.S.

## Slide 10: NWP 12 (cont.)
PCN
  Mechanized land clearing in a forested wetland for the utility line ROW
  Section 10 permit is required
  Utility line in WOUS, excluding overhead lines, exceeds 500 feet
  Utility line is placed within a jurisdictional area (i.e., WOUS), and it runs parallel to a stream bed that is within that jurisdictional area
  Losses of >0.10 acres of WOUS
  Permanent access roads are constructed above-grade in WOUS for a distance of >500 feet
  Permanent access roads are constructed with impervious materials
Note: Temporary losses of WOUS will no longer trigger a PCN requirement on their own

## Slide 11: Waters of the U.S.
All waters which are currently used, or were used in the past, or may be susceptible to use in interstate or foreign commerce, including all waters which are subject to the ebb and flow of the tide
All interstate waters, including interstate wetlands
All other waters such as intrastate lakes, rivers, streams (including intermittent streams), mudflats, sandflats, wetlands, sloughs, prairie potholes, wet meadows, playa lakes, or natural ponds

## Slide 14: Sample USGS Topographic Maps – Marion County, Texas
Submerged wooded marsh or swamp
Perennial River

## Slide 15
Perennial stream
Sample USGS Topographic Maps – Marion County, Texas

## Slide 16: Sample USGS Topographic Maps – Marion County, Texas
Intermittent Stream

## Slide 17: Common JD Problems
Inconsistent data
Wetland delineation only (no streams)
Stream delineation only (no wetlands)
Unclear maps and exhibits
Incorrect coordinates
Wrong form; missing data; incomplete form
Wrong or no stream classification
No photographs; incorrectly labeled photographs

## Slide 18: Problems (cont.)
  No delineation of waters of the U.S. conducted
  Incorrect delineations
  Incorrect determination on permitting options
    Pipelines
    Roads
    Small projects
  Didn’t take into account threatened and endangered species or migratory birds
  Didn’t take into account cultural resources

## Slide 19: Questions
Peter D. McKone, CWB
  Weaver Consultants Group
  pmckone@wcgrp.com
Caleb Watkins
  Summit Midstream
  cwatkins@summitmidstream.com