## Slide 1: Planning, Design, and Installation of a Successful Water Management System to Support a Development Drilling and Completion Campaign
D. Steven Tipton, P.E., SPEC; J. Daniel Arthur, P.E., SPEC; and Mark Faucher
Presented at:
25th International Petroleum
Environmental Conference,
Denver, Colorado
October 30 – November 1, 2018

## Slide 2: Introduction
Water Management Planning and Infrastructure:
  Move from exploration to development
  Pad drilling w/longer laterals
  Move to mostly slickwater fracs
  Increased demand for water for completions
  Water availability
  Induced seismicity
  States limiting disposal capacity
  Environmental concerns
ALL’s holistic approach
  Proven successful and cost effective
Source: ALL Consulting, 2016

## Slide 3: Water Management Plan Components
Water Management Plan
  Company’s acreage position
  Water sources
  Regulatory constraints
  Environmental constraints
  Cultural constraints
  Fracturing fluids
  Water volumes required
  Storage capacity required
  Refill time required
  Layout infrastructure
  Perform ESA
  Geotechnical investigation
  Design storage, treatment facilities, and pipeline
  Construction plan
  Construction execution
Source: B. Pribish, 2015 private communication

## Slide 4: Infrastructure
Infrastructure planning
  Plan placement of
    Fresh water storage
    Produced water treatment facilities
    Disposal facilities
    Buried HDPE pipelines
  Practical limit of lay-flat is about 3 miles
Flexibility
  Move fresh water to any storage facility
  Move treated and produced water from any treatment and disposal facility to any other
  Delivery to and from each facility by both pipelines and trucks
14 miles
14 miles

## Slide 5: Water Needs and Costs
Drilling
  Laterals 5,000 to 12,000 ft.
  Pad drilling
Fracture fluid volumes
  300,000 to 1,000,000 bbls.
Fresh water cost
  Permian
    $0.50 to $0.75 per bbl.
  Anadarko
    $0.25 to $0.50 per bbl.
Costs for produced water treatment
  $0.25 to $1.00 per bbl.
Lower-cost treatment systems
  More interest in recycling

## Slide 6: Fresh Water Availability
Anadarko and Permian Basins typically experience high or extremely high levels of fresh water stress
Permian Basin
  Surface water non-existent
  Productive ground water wells ( 20 – 50 bbl./min)
Anadarko Basin
  Surface water primary source
  Ground water is typically limited
Recycling reduces demand on freshwater

## Slide 7: Baseline Water Stress

## Slide 8: Impoundments
Preferred designs - 1 to 6 lined impoundments
Impoundment liners:
  Geotextile layer with gas vent strips
  Secondary liner
  Geotextile layer
  Leak detection system
    Geocomposite layer
    Sump with washed pea gravel
    Pipe
  Primary liner
Connected by equalization pipes
Suction pipes installed in the clean brine impoundment

## Slide 9: Impoundment Sizing and Design
Impoundment designs based on operators needs:
  Type of water stored
  Completion schedule/water forecast
  Water volume from production
  Water recycling/treatment plan
  Disposal capacity
Ideal Design:
  Can store fresh and produced water
  Effective solids and bacteria removal
  Designed for lowest cost
  Combined storage volume from 1 to 2 million bbl.

## Slide 10: Impoundment Construction

## Slide 11: Water Pit Liner Installation

## Slide 12: Liner Installation/Completed Pits

## Slide 13: Pipeline Design and Installation
Pipeline to transport water
  From water source(s)
  Existing water storage
  Planned storage and treatment facilities
  Provide ability to connect lay flat
  SWD
Multidirectional water flow is a necessity
  50 bbl./min. through 12” HDPE SDR 11
  Transport water from multiple facilities
Developed pipeline system benefits
  Decreases long-term cost
  Increased safety & reduced risk of spills
Automation
  Control of water from the office
  Decrease in-field man power
Notes: .

## Slide 14: Pipeline Installation
October 2018
Copyright © 2018 ALL Consulting

## Slide 15: Pipeline Installation

## Slide 16: Drivers for Recycling
Demand for recycling of produced water is expanding
Reduce demand on limited freshwater resources
Reduce injection volumes
  Reduce injection costs
  Limited disposal zones for Class II wells
  Induced Seismicity concerns
Reduce costs of fresh water
Source: ALL Consulting, 2018

## Slide 17: Recycling Objectives
Produced water that can be used as a base fluid for hydraulic fracturing
  Produce clean brine
  Economical
Treatment process must be able to remove
  Hydrocarbons
  Metals
  H2S
  Iron sulfide
  Bacteria
  Suspended solids
Treatment process must be able to handle variable qualities of inlet water
Treatment must be economical compared to the acquisition and disposal of fresh water

## Slide 18: Recycling Challenges
Produced water
  Produced water use must be economically feasible
  Minerals in the water can interfere with friction reducers or frac gel
  Water quality varies widely
  Minerals in the water can cause scale
Environmental regulations
  More stringent
  In most states flowback, recycle or produced water pits have to be permitted in some fashion
  OK requires design, certification, permitting, and construction supervision by a registered professional engineer

## Slide 19: A Basic Approach that Works
Combine at the same facility
  Produced water treatment
  Class II SWD well
  Multiple facilities strategically placed
Separate pipelines
  Fresh water
  Produced water
  Clean brine
Tank battery to remove solids and separate oil
Treatment system to provide a clean brine
Injection well for produced water that cannot be recycled
Source: ALL Consulting, 2017
Source: ALL Consulting, 2017

## Slide 20: Treatment System
Treatment system consists of:
  Series of lined impoundments
  Aeration and microbial treatment
  Equalization pipes
  Multiple impoundments
    Improve treatment
    Provide ample storage
Results in a clean brine suitable for reuse
Source: ALL Consulting, 2016

## Slide 21: Tank Batteries
Located adjacent
  Injection wells
  Treatment pits
Remove
  Solids
  Separate oil (30 ppm)
Automated to send water
  Treatment pits
  Injection well
  Both
Typically coupled with 2 H-pumps
H-Pumps controlled by variable speed drives (VSDs)
Source: ALL Consulting, 2017
Source: ALL Consulting, 2017

## Slide 22: Impoundment Aeration / Biological Treatment
Aeration
  Increases dissolved oxygen (DO) levels in water water
  DO + food source (hydrocarbons) sustain aerobic bacteria
  Eliminates hydrocarbons and other organics from the water
  Prevents water from “Flipping”
  Reduces the proliferation of Anaerobic Bacteria
Aerobic bacteria
  Control anaerobic bacteria
  Manage with biocides during frac operations
Anaerobic bacteria
  More problematic (e.g., SRB’s create H2S / Souring)
  More expensive to manage with biocides

## Slide 23: Disposal Considerations
Increase in seismicity
  Decreased injection allowables
  Operators are choosing to limit injection
  Alternate disposal zones are limited
Trucking produced water for disposal
  Expensive
  Can create adverse community impacts
Operators explore recycling as a way to reduce injection volumes

## Slide 24: Typical Water Disposal Facility
October 2018
Copyright © 2018 ALL Consulting

## Slide 25: Benefits of the Approach
Ensures adequate water for completions
Allows for
  Unexpected changes in the completion schedule
  Changes in frac water volumes
Reduces fresh water demand
Provides options for managing produced water
Reduces SWD well injection volumes
Limits trucking for produced water disposal

## Slide 26: Keys to Success
Provide a cost-effective holistic approach to water management by
  Reducing fresh water demand
  Sufficient water supply for completions
  Recycling produced water
  Disposal of excess water
Provide flexibility to respond to unexpected changes
  Schedules
  Move water from one facility to another
  Injection well problems
  Equipment failures
Simple operations
  Automated controls
  Uncomplicated treatment system
  Limit operator involvement in day-to-day operations
  Minimal operator training required
Capital investment costs are typically recovered in three years or less.

## Slide 27: Questions?

## Slide 28
Citation Information:
Tipton, D. Steven; J. Daniel Arthur; and Mark Faucher. “Planning, Design, and Installation of a Successful Water Management System to Support a Development Drilling and Completion Campaign.” Presented at the 25th International Petroleum Environmental Conference, Denver, Colorado, October 30 –November 1, 2018.
Contact Information D. Steven Tipton, P.E., SPEC Senior Engineer ALL Consulting Tulsa, OK stipton@all-llc.com