## Slide 1: Small Footprint LRP® Pumping Unit
Jordan Hanson, Control Solutions, Unico Oil & Gas
Ron Peterson, Control Solutions, Unico

## Slide 2: Unico LRP® Pumping Unit
Pumping Unit for Sucker Rod
Replaces Traditional Horse Head
Electromechanical (Not Hydraulic)
Small Size and Weight
Safety: No Exposed Moving Parts or Pinch Points
Ease of Transportation / Installation
Visual Appeal
Quiet Operation
Reduced Environmental Impact

## Slide 3: Unico LRP® Pumping Unit
Replaces Traditional Pumping Unit

## Slide 4: Unico LRP® Pumping Unit
Minimal Environmental Impact during Installation and Operation
Two Units Transported on a Flat Bed

## Slide 5: Unico LRP® Pumping Unit
LRP® System Comprises:
Reversing AC Motor
Gear Reducer
Rack and Pinion Drive Assembly
Mounting Stand
Control System

## Slide 6: Conventional Well Completion
Conventional Well Completion / Traditional Downhole Sucker Rod Pump
Conventional Wellhead
Conventional Stuffing Box
Casing and Tubing Mount Options Available
Mounting Stand Provides Access to Stuffing Box and Tree
Polished Rod Optionally Enclosed (Screened)

## Slide 7: Unico LRP® Pumping Unit
Before
After

## Slide 8: Example Installations / Environmentally Sensitive Sites

## Slide 9
Example Installations / Environmentally Sensitive Sites

## Slide 10
Technical Specifications
Light Duty
Rated Lifting Capacity: 4,800 lbs.
Rated Gearbox Torque Capacity: 8,500 in-lbs.
Rated stroke (in.) | 12 | 24 | 36
Weight (lbs.) | 511 | 534 | 566
Overall height above stand (in.) | 75 | 99 | 123

## Slide 11
Technical Specifications
Standard Duty
Rated Lifting Capacity: 12,000 lbs.
Rated Gearbox Torque Capacity: 23,900 in-lbs.
Rated stroke (in.) | 20 | 32 | 44 | 56
LRP weight (lbs.) | 806 | 1197 | 1232 | 1272
Overall height above stand (in.) | 95 | 120 | 143 | 166

## Slide 12
Technical Specifications
Heavy Duty
Rated Lifting Capacity: 19,000 lbs.
Rated Gearbox Torque Capacity: 38,100 in-lbs.
Rated stroke (in.) | 32 | 44 | 56
Weight (lbs.) | 1823 | 1923 | 2023
Overall height above stand (in.) | 144 | 186 | 197
Rated stroke (in.) | 64 | 86
Weight (lbs.) | 2325 | 2735
Overall height above stand (in.) | 299.5 | 339.5

## Slide 13
Technical Specifications
Tandem Heavy Duty
Rated Lifting Capacity: 38,100 lbs.
Rated Gearbox Torque Capacity: 76,200 in-lbs.
Rated stroke (in.) | 86 | 100 | 120 | 144
Weight without motors (lbs.) | 2500 | 2630 | 2810 | 3035
Maximum clamp height above stand (in.) | 237.6 | 266.9 | 306.0 | 354.9

## Slide 14
Dual Completion
Independent Production from Two Zones
One Wellhead
Dual Tubing / Rods
Dual Pumps
Packer Isolation

## Slide 15
Automation / Controls
Near Unity Power Factor
IEEE-519 Harmonic Compliant Options
Optimization Controls for Efficiency:
  Controls from Down-Hole States / Potential Energy Savings as Unit Runs No Faster than Necessary to Match Well Inflow – No “Extra” Strokes for Improved Efficiency.
Remote Telemetry / Operation and Surveillance / Troubleshooting:
  Reduced Pumper Visits to Wellsite
  Efficiently Dispatch Appropriate Service Personnel to Wellsite

## Slide 16
Automation / Controls
Rapid Fault Detection with Alarm / Callout:
  Well Fluid Leak Detection
  Tubing Pressure
  Casing Pressure
  Overload
  Underload
  Etc.

## Slide 17
GMC™ Remote Telemetry

## Slide 18
Camera Surveillance

## Slide 19
Gen III
Next Generation Design for Added Durability and Leak Resistance:

## Slide 20
Thank you. Questions?