## Slide 1
Successful On-Site Treatment of Oil-Impacted Soil and Oil Sludge Using STARx/Hottpad™ (Ex Situ Smoldering)
Presented by: Gabriel Sabadell, Ph.D., PE

## Slide 2: Overview
Smoldering Combustion Basics
Case Study
  Full-scale application to treat oil-impacted soils and sludge at an active terminal facility in SE Asia
Summary
Acknowledgments:
  Savron – Cody Murray, Grant Scholes, Gavin Grant, & Dave Major
  Chevron ETC – Dave Thomas & Paul Bireta

## Slide 3: Smoldering Combustion
Exothermic reaction converting carbon compounds to CO2 + H2O
Fuel
Heat
Oxidant
Smoldering is possible due to large surface area of organic liquids (e.g., NAPL) within the porous matrix
Combustion
Oil-Impacted Soil or Organic Waste
Injected Air
Heater Element (for ignition only)

## Slide 4: Overview of Hottpad Treatment
Video accelerated 50 times

## Slide 5: Case Study
5
Active terminal facility in south east Asia
Designed to treat 3,500 m3 of
stockpiled API separator sludge
Co-treatment with Oil-impacted site soils

## Slide 6: System Overview
  Fixed 6 pad system
      78m2 surface area
Heating
Element
Air Injection Pipe
4.2 x 2.8 m

## Slide 7: System Components
Fixed, 3 m walls
Deployable cover system
System Overview

## Slide 8: Emissions Collection

## Slide 9: Mixing/Loading
  >25% sludge by volume
  2 m high (160 m3)
  0.5 m cover material
System Loading

## Slide 10: Process Monitoring
Ignition and Combustion Tracking
  Real time thermocouple and combustion gas analysis
Process Equipment Monitoring
  Flow and pressure monitoring
  Vapor treatment system monitoring
  Power and control system monitoring/optimization
Treatment Monitoring/Efficiency
  Pre/post laboratory analysis
Hottpad Full-Scale Operations - Processing
O2 (%)
CO2 (%)
CO (ppm)
THC (ppm)

## Slide 11: Process Monitoring

## Slide 12: Treatment Results
Before
After

## Slide 13: Treatment Results
Wet areas from water spray for dust suppression
Controlled emissions capture
  Extraction ~ 1.25 times Injection rate
4-4.5 days for treatment
  Includes ignition time
No issue with wall temperatures
Compound | “Before” Concentration (mg/kg) | “After” Concentration (mg/kg)
BTEX | ND | ND
TPH C6-C9 | ND | ND
TPH C10-C14 | 356 | ND
TPH C15-C28 | 25,400 | ND
TPH C29-C36 | 9,750 | ND
Total | 35,506 | ND

## Slide 14
Clean Soil
Oil-Impacted Soil
Hottpad Treated Soil
Plant Growth
Fertilizer
No Amendments

## Slide 15: Example – Process Optimization
Base Case
  Operate all pad heaters simultaneously
  High peak load during heating, followed by low demand for duration of process
“Rolling Start”
  Sequenced heater operation
  Reduced peak power
  Steadier power load
  More efficient service sizing

## Slide 16: Conceptual Plant with 4 Base Systems
Gained Efficiencies
  Continuous operations
  Centralized controls
  Single emissions collection system

## Slide 17: Technology Cost Drivers
Capital
  Hottpad system
  Emissions treatment system
Throughput
  Treatment propagation rate
  Size of system (scalable)
Energy Requirements
  Heaters
    Electric or gas
    Peak demand vs total demand
  Blowers
  Emissions treatment
    Additional fuel
Project Cost Analysis

## Slide 18: Summary
Technology works well for a wide range of materials
  Can combine sludge with contaminated soil
  Contaminant destruction
Cost-effective as compared to other alternatives
Scalable for on-site remediation
  Reduce/eliminate truck transport
More environmentally friendly
  Soil reuse (construction backfill or revegetate)
  Smaller GHG footprint
  Limited waste by-products
From Prototype to Full-Scale

## Slide 19
Questions?
gsabadell@savronsolutions.com